THIS IS A PRACTICE ASSESSMENT. Show formulas, substitutions, answers (in spaces provided) and units!

The following questions are about fossil fuel energy production.

1.	Draw a Sankey diagram for a coal-fired plant. Begin with coal, and end with electricity at the home.

2.	Suppose a steam locomotive is rated at 7500 horsepower.  If its efficiency is 6%, how much wood must be burned in a 3 hour trip? 1 hp = 750 W. Wood has an energy density of 20.0 MJ kg-1.								  2. _________________

A 95.0 MW coal-fired power station is proposed for a city. It is expected to have an efficiency of about 15.5%, and use a coal with an energy density of 35.0 MJ kg-1.

3.	Calculate the mass of coal that must be burned per day to provide the desired output power.			  3. _________________

4.	How many train cars per day are needed to keep this plant supplied with coal if each car holds 2.5 metric tons of coal? 							4. _________________

The following questions are about nuclear power.

5.	If a nuclear power plant powered by uranium-235 has the same output and the same efficiency as the coal-fired plant of the previous problem, how many kg of nuclear fuel will it burn per year?

5. _________________

6.	Discuss the role of the moderator and the control rods in the production of controlled fission in a thermal fission reactor.

_____________________________________________________________________________

The following questions are about hydroelectric power systems.

7.	Why is a dam a good component in a power grid?

_____________________________

_____________________________

_____________________________

8.	Calculate the potential energy yield of this hydroelectric scheme.		8. _________________

9.	If the water flow rate is 15 m3 per second, what is the power provided by the moving water?

9. _________________

A wind turbine has a blade length of 14.0 m. Before the air strikes the blades it has a speed of 18.0 ms-1 and a density of 1.15 kg m-3. After passing through the blades, the air has a speed of 6.50 ms-1 and a density of 1.45 kg m-3. The efficiency of the turbine is 16.2%.

10.	Find the power carried by the air before striking the blades.

10. _________________

11.	Find the power carried by the air after passing through the blades.

11. _________________

12.	Find the power output generated by the wind turbine.			12. ________________

A photovoltaic cell on a calculator has an area of 4.00 cm2 and an efficiency of 6.75%. The cell is placed in a position where the sun's intensity is I = 750. W m-2.

13.	What is the power output of the cell?			13. ________________

14.	If the cell is rated at 0.500 V, what is its current output?	14. ________________

15.	How many of the cells would you need to supply a current of 10.0 A? How would you connect the cells?									15. ________________

The following questions are about solar heating panels.

16.	Distinguish between a photovoltaic cell and a heating panel.

___________________________________________________________________________

17.	A solar heating panel has an efficiency of 25.0%. If the panel is placed in a position where the sun's intensity is I = 750. W m-2over an 8.00-hour period of the day, and is required to raise the temperature of 30.0 kg of water by 12.0° during that time, what must its area be? Recall the c = 4186 J kg-1 K-1.								17. ________________