THIS IS A PRACTICE ASSESSMENT. Show formulas, substitutions, answers (in spaces provided) and units!

A rectangular coil of wire having dimensions 4.5 cm by 6.8 cm has 135 turns. It is rotating at a frequency of 60 Hz in a magnetic field having a strength of 2.5 T.

1.	What is its peak voltage (0?							1. _________________

2.	Write the equation of the time dependence of its emf.		2. ________________________

3.	If the frequency is decreased to 40 Hz, what is this generator’s peak voltage?

3. _________________

The graphs of voltage and current for an ac circuit containing a resistor are shown.

4.	Find the rms voltage corresponding to the induced emf whose graph is shown.

4. ________________

5.	Find the peak voltage.	5. ________________

6.	Find the angular frequency of the coil that is producing this emf.		6. ________________

7.	Find the maximum flux linkage of the coil that is producing this emf.		7. ________________

8.	Find the rms current from the graph.

8. ________________

9.	Find the peak current.							9. _________________

10.	Write the equation which shows the time variation of the current.	10. _______________________

11.	Find the resistance of the circuit.						11. ________________

12.	What is the average power dissipated by the circuit?			12. ________________

A transformer having 145 turns in its primary winding has a 60 Hz input voltage of Vin = 75 VAC. It is desired that Vout  should be 120 VAC.

13.	How many turns should the secondary winding have?

13. ________________

14.	If the current in the primary winding is 1.25 A, what will the current in the secondary winding be?							14. ________________

The following questions are about power transmission and the power grid.

15.	Explain the use of high-voltage step-up and step-down transformers in the transmission of electrical power.   ___________________________________________________________________________

__________________________________________________________________________________

16.	A power plant produces a 60 Hz alternating voltage having Vrms = 125 V. A step-up transformer is needed to raise the plant’s voltage to 765 kV. Find the ratio of Ns / Np needed in the transformer.

16. ________________

A power transmission cable having a diameter of 4.75 cm is made of aluminum which has a resistivity of 5.18(10 -8 (m.

17.	Find the cross-sectional area of the cable in m2.				17. ________________

18.	Find the resistance of this cable if it provides electricity to a township 375 km away from a power plant.									18. ________________

19.	Suppose this cable is used to supply a township with 285 MW of energy at a transmission voltage of 765 kV. What is its current? What is its heat loss. What percentage of the overall energy transmission is this?							19. ________________

________________

________________

A circuit that consists of four diodes and a resistor is shown.

20.	Label the top AC power supply terminal with a (+), and with a red pencil trace the positive current through the circuit all the way to the load resistor and the correct DC output terminal.

20. ___See figure___

21.	Label the bottom AC power supply terminal with a (–), and with a green pencil trace the negative current through the circuit all the way to the load resistor and the correct DC output terminal.

21. ___See figure___

22.	If the AC power supply now reverses its polarity, determine which output terminal is (+) and which is (–).										22.          TOP is_______

BOTTOM is_______

# Text boxes

15

20

10

5

-2

-1

2

1

0

I / A

t / ms

15

20

10

5

-40

-20

20

10

0

em f  / V

t / ms